SECTION 044200

EXTERIOR CLADDING

BASIS OF DESIGN – PROBE/FISCHER ACT SYSTEM

Provide aluminum support system consisting of the following:

- Curved 6 hole horizontally slotted  load bearing U shaped wall holders designed to compensate for connection to uneven sub structure surfaces. Provide a plastic thermal break disc between wall holders and structure of building.  For metal studs, we offer a three  hole pattern with continuous  L or T angles.

- Curved U shaped sliding point wall holders used for wind and lateral load bearing.  Wall holders contain 2 to 4 horizontally slotted holes for connection to sub structure.  Must have 15mm long vertical slotted holes to allow for thermal expansion.  For metal studs, we offer a three hole pattern with continuous  L or T angles that fastens right to the metal stud.

- Box style 50mm wide 4 wall aluminum vertical support stud profiles. For metal studs, we offer continuous L or T angles.

- Connection of vertical profile to curved U shaped wall holder with approved stainless steel fasteners only.

- Closed box shaped horizontal profiles with vertical stem to accept stone connection brackets. Minimum of 2 horizontal profiles per panel.

- Connection of horizontal profiles to vertical profiles is achieved by clamping two profile guidance brackets to allow for thermal expansion and contraction forces.  Horizontal profiles must not be directly fastened to the vertical profile.

- Provide splice plate for connection of horizontal profiles.  Note only one end of the splice plate must be directly fastened.

- Probe/FZP stainless steel undercut anchors located at minimum 1/5 of panel dimensions relative to all four sides of each panel.

- Stone anchor must show technical approval for use in natural stone such as ETA – 11 /0145 ** e

- Stone panel tolerance not to exceed +/- 1/16

- The complete system must demonstrate a  minimum 10 year successful performance track record in US projects.

FOR INFORMATION AND PRICING – CONTACT louisa@probefacadesystems.com

© Copyright 2013 PROBE Rainscreen Facade Systems.

www.PROBEFACADESYSTEMS.com